## Slide 1
Ph.D. Synopsis Seminar
on
By
Anik Kumar Samanta
(16AT91R11)
Under the supervision of
Prof. Aurobinda Routray
&
Prof. Swanand R. Khare
Advanced Technology Development Centre
Indian Institute of Technology Kharagpur
January 2021
Frequency Estimation under Stationary and Non-stationary Conditions - A Case Study of Induction Motor Fault Diagnosis

## Slide 2
Stationarity
2/36
Stationary process
A stochastic process is said to be a stationary if it’s statistical properties are time-invariant. This is stationarity in strict sense. Mathematically,
Wide sense stationarity (WSS)
A stochastic process is WSS if it’s mean is constant and autocorrelation depends only on the delay. Mathematically,
Joint stationarity
and have the same joint statistics of and . Mathematically,
“Majority of non-stationarities are due to temporally unstable variance and/or frequency”, Chau’05

## Slide 3
Low amplitude
Variable frequency & load torques
Exact amplitude & decision rule
Detection of stationarity
Stationary segmentation
Parameter estimation under non-stationarity
Accuracy
Resolution
Noise Robustness
Execution Time
Accuracy
Chirp rate
Abrupt changes
Noise Robustness
Motivation and Objective
3/36
*SCIM: Squirrel Cage Induction Motor
Objectives of the research
Detection and estimation of sinusoidal parameters under stationary as well as non-stationary conditions, and its application in diagnosing weak faults of SCIMs.
Spectral
Estimation
Assumption of stationarity
Instantaneous frequency estimation
Fault detection of SCIMs*

## Slide 4
Stationary
Non-stationary
Frequency Estimation
Rayleigh Quotient (P1)
Bayesian
MAP (P6)
Constrained Kalman Filter (P2)
Scope, Outline, and Overview of the Research
Statistical comparison
Noise Analysis
Resolution Analysis
Statistical comparison
Noise Analysis
Resolution Analysis
Estimate frequencies of multiple time-varying components simultaneously
Statistical evaluation
Gravitational waves for black hole merger
Detect SCIM faults from vibration (P4)
Implementation for IoT-based fault detector using stator current (P7)
Suppression of multiple dominant components (P3)
Minimum distance detector for inherent fault component (P5)
Hypothesis testing and automatic thresholding

## Slide 5
Classical
High Resolution
Limited Resolution
Spectral Estimator
Parametric
Eigen-based [Hoang’17]
DFT
Periodogram
Modified-periodogram
ARMA-spectrum
AR-spectrum
MA-spectrum
Classical
Bayesian [badiu’17]
Tikhonov
Gaussian
Bernoulli-Gaussian
MAP [Fu’07]
MMSE
Sparse-Bayes L1
ESPRIT
MUSIC
Proposition 1: Rayleigh Quotient
Proposition 2: Gauss-Markov Bayes MAP
Accurate frequency estimation
Noise robust
Accurate amplitude
Accurate frequency estimation
High resolution
Recursive
Spectral Estimators – Review
ARMA – autoregressive moving average
MUSIC – Multiple signal classifier
ESPRIT – Est. of signal parameters via rotational invariance
MAP – Max. a-posterior estimate
MMSE – Minimum mean square error estimate

## Slide 6
P1: Rayleigh-Quotient based Spectral Estimator
6
Estimation of accurate amplitude
let us assume that the input signal consists of only a single component given by
Presence of a sinusoid at will contribute to a peak (eigenvalue), given by , due to eigenvector
Development of spectral estimator
and
If is a symmetric matrix with eigenvector , there exist a corresponding eigenvalue σ, that can be approximated using the theory of Rayleigh quotients (Datta’10, Pg. 301-304) by
and is the additive noise
AK Samanta, A Naha, A Routray, AK Deb, "Fast and accurate spectral estimation for online detection of partial broken bar in induction motors", Mechanical Systems and Signal Processing, 2018

## Slide 7
Statistical Evaluation of the Spectral Estimator
Decision statistic:
Fig. 1 Probability of resolution for (A) Autocorrelation matrix size (B) SNR level (C) Sampling frequency
A
B
C
Fig. 2 Propagation of frequency estimate error with (D) SNR level (E) Autocorrelation matrix size
Fs = 1000Hz
Fs = 1000Hz
L = 1000
;
Fig. 3 Mean Execution time over 100 runs for each autocorrelation matrix size
System Specification:
Processor: Intel Xeon 2.80 GHz
RAM: 16 GB
OS: Windows 7 (Professional)

## Slide 8
1970
STFT
Wavelet
1980
Wigner Distribution
Late 1980
Use of phase
1990
Spectrogram
Scalogram
Limited resolution
Cross term for multiple components
Synchro-squeeze (SST) [Oberlin’15]
Reassignment [Auger’13]
Limited resolution
Indirect method
Window selection not based on chirp-rate, resolution.
Instantaneous Frequency Estimation - Review

## Slide 9
Late 2000
Empirical Mode Decom.
Kalman Filters [Routray’02]
Present
Modified SST
Variational Mode Decom.
Late 1990s
S-transform
Fractional Fourier Transform
Time (s)
Frequency (Hz)
Kalman Filter
Instantaneous Frequency Estimation - Review
Window selection based on chirp-rate, resolution for single component
Recursive, single Component Estimation
Physical significance of mode is complex
High resolution, but error prone
*Image source: “Agile photonic fractional Fourier transformation of optical and RF signals”, Optica 4.8 (2017): 907-910.
*
Pros:
High-resolution
Multiple time-varying components
Provision for model (more accurate)
Handle abrupt changes
Cons:
Parameter initialization
Low-SNR accuracy
Proposed Method

## Slide 10: P2: Real-time Estimation of Multiple Time-varying Frequency Components
Signal Model
 | Amplitude
 | Normalized inst. frequency
 | Phase
 | White Gaussian noise
 | Number of components
 | Amplitude
 | Normalized inst. frequency
 | Phase
 | White Gaussian noise
 | Number of components
Represent as an AR process by assuming a frozen state with constant coefficients for short duration for slowly-varying signals [9] as
Taking z-transform, we have:
For-components:
Therefore,
Hence,
Inverse z-transform:
AK Samanta, A Routray, SR Khare, A Naha, "Direct estimation of multiple time-varying frequencies of non-stationary signals", Signal Processing, 169, 107384, 2020.

## Slide 11: Observation and State Models
Observation Model:
States:
State Propagation – Gauss-Markov Random Walk:
Linearization with Taylor expansion:

## Slide 12: P3: Real-time Estimation and Elimination of Multiple Dominant Components
(b)
Fig. 1 Spectrum analysis of motor vibration (a) before and (b) after signal conditioning.
Algorithm: Elimination of dominant frequencies
AK Samanta, A Routray, SR Khare, & A Naha, “Minimum Distance-based Detection of Incipient Induction Motor Faults using Rayleigh Quotient Spectrum of Conditioned Vibration Signal”, in IEEE Transactions on Instrumentation and Measurement , 2021.

## Slide 13: IF Estimation – Simulated Results
Fig. 3 Estimation of cross-over frequencies
Fig. 1 Distant frequency estimation
Fig. 2 Closely spaced frequency estimation
SNR = 40 dB
Fs = 200 Hz
Key observation:
Frequency estimates don’t cross

## Slide 14: IF Estimation – Statistical Results
Fig. 1 NMSE for frequency estimation at different (A) SNR levels and (B) Chirprate
with 1000 Monte-Carlo simulations.
Fig. 2 NMSE versus variation of frequency difference with 1000 Monte-Carlo simulation (SNR = 60 dB).
Fig. 3 Abrupt change in a frequency component
A
B
Fig. 4 Accuracy of frequency estimate with abrupt change

## Slide 15: Real-world Examples: Bat-signal and GW-wave Analysis
Fig. 1 Time-frequency analysis of the popular ’Batsignal’, an echolocation
pulse emitted by a big brown bat
Fig. 2 Frequency estimation for the binary black-hole collision event GW150914 observed at Hanford, Washington (H1)
Key observation:
Three components detected and estimated
Key observation:
Smoother estimate of different phases

## Slide 16: Real-world Examples: Supply Frequency Estimation
Fig. 1 Estimation of abrupt change in fundamental supply frequency using stator current of a squirrel cage induction motor. The temporal resolution during the initial stages of the abrupt change is depicted in the inset in log-scale.
Key observations:
Fast response
Drive dynamics captured

## Slide 17
State of the Art for IM Fault Diagnosis
Fatigue
Inherent eccentricity
Flaking and spalling due to small metal parts
Manufacturing defects
Contamination and abrasion
Bearing current
Improper lubrication
Cause
Vibration
Modulated stator currents
Torque pulsation and reduced average torque
Rotor speed pulsation and low average speed
Excessive heating
Symptoms
Technology
Power Spectral Density (PSD)
Multiple Signal Classification (MUSIC) [Nandi’05, Naha’16]
ESPRIT
Wavelet Decomposition
Synchrosqueeze [Tu’19]
Pattern Recog [Panderkone’19]
Deep learning [Zhao’19]
Signatures used
Acoustic
Vibration
Stator Current
Magnetic Field
Supply Voltage
Active-Reactive Power
Thermal Field
Thermal Imaging [Prieto’18]
Stator faults
Rotor faults
Bearing faults
Inter-turn
short circuit
Broken rotor bar
Broken End Ring
Eccentricity
Induction motor weak faults
Inner Raceway
Outer Raceway
Cage fault
Rolling element
[Riera-Guasp’15]
Notes: 1. Esprit: estimation of signal parameters via rotational invariance techniques
2. Why stator current and why MUSIC??

## Slide 18
Experimental Setup (22kW IM-24kW DC Gen)
Induction Motor
DC Generator
Cooling Arrangement
AC Tacho Generator
(A) Induction Motor - DC Generator Set
For generating various base and fault signatures, testing and validation of algorithms in lab
Host
Sensor
Target
(C) Sensor-Target Interface
Specification of the Experimental Setup | 
Rated voltage | 415V
Rated current | 40.5A
Number of poles | 4
Rated power | 22kW
Number of phases | 3
Number of rotor bars | 28
Vibration sensor location
(B) Panel Board
IM V/F control
IM indicating instruments
DC generator control and indicating instruments
Load switches

## Slide 19: Introducing Faults
Fig. 1 Spark electric discharge
machining
Fig. 3 Outer Raceway Fault
Fig. 2 Inner Raceway Fault
Fig. 4 Rolling Element Fault
Fig. 5 Half broken rotor bar
Fig. 6 Full broken rotor bar

## Slide 20: P4: Vibration Analysis with Rayleigh Quotient
Fig. 1 Spectrum of the conditioned vibration signal obtained from the lab-setup, with inner-race fault for different load levels.
Fig. 2 Spectrum of the conditioned vibration signal obtained from the lab-setup, with outer-race fault for different load levels.
Key observations:
Prominent fault component
Matches theory
Key observations:
Prominent fault component
Matches theory

## Slide 21: Vibration Analysis with Rayleigh Quotient
Fig. 2 Spectrum of the conditioned vibration signal obtained from the lab-setup, with broken rotor bar fault for different load levels.
Fig. 1 Spectrum of the conditioned vibration signal obtained from the lab-setup, with cage fault for different load levels.
Key observations:
Signal conditioning improves detection
Matches theory
Key observations:
Inadvertent fault
High-load prominence
Matches theory

## Slide 22: P5: Minimum Distance-based Detection
Conventional:
Our proposition:
Parameter Estimates under each Hypothesis:
The linear model:
Probability density function:
AK Samanta, A Routray, SR Khare, & A Naha, “Minimum Distance-based Detection of Incipient Induction Motor Faults using Rayleigh Quotient Spectrum of Conditioned Vibration Signal”, in IEEE Transactions on Instrumentation and Measurement , 2021.

## Slide 23: Implementation, Simulation and Practical Results
Spectral Estimation
Pre-processing
Peak Detection
Simulation Results:
Input
Faulty
Healthy
=5
Simulation parameter
Fault type | Accuracy (%) | 
 | Lab Data | CWRU Data
Broken rotor bar | 95.09 % | Not available
Rolling Element | 98.44 % | 100 %
Cage defect | 98.36 % | 100 %
Inner Raceway | 90.33 % | 100 %
Outer raceway fault | 96.77 % | 100 %
Fault Detection
Accuracy:
+

## Slide 24: P6: Bayesian MAP Sequential Spectral Estimation
Signal Model
 | Amplitude
 | Normalized instantaneous frequency
 | Phase
 | White Gaussian noise (observation)
 | Number of components
 | Amplitude
 | Normalized instantaneous frequency
 | Phase
 | White Gaussian noise (observation)
 | Number of components
Likelihood:
Prior PDF:

## Slide 25: Maximum a Posteriori Estimate
Posterior PDF:
Find:
Recursive estimation of associated parameters:
Power Spectrum
Solution:

## Slide 26: Algorithm Implementation and Key Observations
Frequency (Hz)
Normalized Power
Normalized Power
Low Order = 10
High Order = 100
Some observations
1. The lobe-width is high with low orders
2. With low-order, the accuracy increases with increase in observations.
3. Multiple peaks appear with increased order
4. The spurious peaks disappear with increased observation
5. Lobe-width decreases, Resolution improves

## Slide 27: Statistical Results
Fig. 1 Spectral estimation with different methods. N = 100, f1 = 50Hz, and SNR = 3 dB.
Fig. 2 Mean squared error variation with data length. SNR = 6.98 dB
Fig. 3 Mean squared error variation with the signal to noise ratio. N = 1000
Fig. 4 Variation of the probability of resolution of two sinusoidal components with different model-order.

## Slide 28: Results-SCIM Fault Diagnosis
Fig. 1 BRB Fault (A) Low Load (B) High Load
Fig. 2 Cage Fault (C) Low Load (D) High Load
A
B
C
D

## Slide 29: Results-SCIM Fault Diagnosis
Fig. 1 Inner-raceway (A) Low Load (B) High Load
Fig. 2 Outer-raceway (C) Low Load (D) High Load
B
C
D
A

## Slide 30: Progression of Fault Diagnosis Systems
Fig. 1 The online fault detection system and its console system
Fig. 4 Mobile phone based fault detector
Fig. 3 The offline fault analyzer
Fig. 5 Cloud-based implementation with in-house WiFi current sensors
Fig. 2 Raspberry pi implementation
SCIM fault model developed with nine faults with real-time simulation
Methods developed to detect SCIM faults in transient and steady state conditions
A low complexity method developed for continuous online condition monitoring
A mobile application developed for SCIM health assessment in the absence of dedicated hardware and processing platforms

## Slide 31: P7: IoT-based Fault Detection System
IOT-based hardware framework used for fault detection
Implementation of the algorithm
Server
Client: User

## Slide 32
Stationary
Non-stationary
Frequency Estimation
Rayleigh Quotient
Bayesian
MAP
Constrained Kalman Filter
Fast and accurate frequency estimation
Noise-robust
Accurate amplitude estimation
Analyzed bearing faults using vibration
High-resolution, recursive, and accurate frequency estimation
Analyzed SCIM faults stator current
Implemented for IoT-based fault detection unit
Conclusions
Accurate frequency estimation of multiple time varying components
High resolution
Recursive
Can handle abrupt changes in frequency
Suppression of multiple dominant components (SCIM signal conditioning)
Amplitude estimation is required
Performance under low-SNR to be improved
Pros:
Low resolution
Cons:

## Slide 33: Organization of the Thesis
Chapter 1: Introduction
Chapter 2: Direct Estimation of Multiple Time-varying Frequencies of Non-stationary Signals
Proposes a generalized framework for real-time tracking of multiple time-varying sinusoidal frequencies of a non-stationary signal.
Chapter 3: Rayleigh Quotient Spectrum for Online Detection of Partial BRB in SCIM
Introduces the Rayleigh-quotient-based spectral estimator and uses it for detecting partially broken rotor bar faults using stator current. It also describes the SCIM experimental setup
Chapter 4: Minimum Distanced Fault Detector using Rayleigh Quotient Vibration Spectrum
Extends the IF-estimator to eliminate multiple dominant components. Uses minimum distance-based hypothesis test for fault detection. Detects multiple SCIM faults using Rayleigh-quotient spectrum of vibration
Chapter 5: Bayes Maximum a-Posterior Spectral Estimation for Stator Current Analysis
Proposed a Bayesian MAP-based sequential spectral estimator for detecting SCIM faults using a single-phase stator current input.
Chapter 6: Embedded Fault Detection System Development
Chapter 7: Conclusions and Future Research Directions

## Slide 34: Publications from the Thesis
Patent (Filed):
A. Routray, A. Naha, AK Samanta, Amey Pawar, Chandrasekhar Sakpal, “A system for assessment of multiple faults in induction motors”, WO2019167086A1, 2019
Journals:
AK Samanta, A Routray, SR Khare, & A Naha, “Minimum Distance-based Detection of Incipient Induction Motor Faults using Rayleigh Quotient Spectrum of Conditioned Vibration Signal [Accepted]”, in IEEE Transactions on Instrumentation and Measurement
AK Samanta, A Routray, SR Khare, A Naha, "Direct estimation of multiple time-varying frequencies of non-stationary signals", Signal Processing, 169, 107384, 2020.
AK Samanta, A Naha, A Routray, AK Deb, "Fast and accurate spectral estimation for online detection of partial broken bar in induction motors", Mechanical Systems and Signal Processing, 2018
Journal under preparation:
Sequential Maximum a-Posterior Spectral Estimation for IoT-based Fault Detection of Squirrel
Cage Induction Motors

## Slide 35: Bibliography
[Auger’13] F. Auger, P. Flandrin, Y.-T. Lin, S. McLaughlin, S. Meignen, T. Oberlin, and H.-T. Wu, “Time-frequency reassignment and synchrosqueezing: An overview," IEEE Signal Process. Mag., vol. 30, no. 6, pp. 32-41, 2013.
[Chen’10] C. Chen, G. Chang, R. Hong, and H. Li, “Extended real model of Kalman filter for time-varying harmonics estimation,” IEEE Trans. Power Del., vol. 25, no. 1, pp. 17-26, 2010.
[Hlawatsch’13] F. Hlawatsch and F. Auger, Time-frequency analysis. John Wiley & Sons, 2013.
[Jensen’17] T. L. Jensen, J. K. Nielsen, J. R. Jensen, M. G. Christensen, and S. H. Jensen, “A fast algorithm for maximum-likelihood estimation of harmonic chirp parameters," IEEE Trans. Signal Process., vol. 65, no. 19, pp. 5137-5152, 2017.
[Oberlin’15] T. Oberlin, S. Meignen, and V. Perrier, “Second-order synchrosqueezing transform or invertible reassignment? towards ideal time-frequency representations." IEEE Trans. Signal Process., vol. 63, no. 5, pp. 1335-1344, 2015.
[Routray’02] Routray, A., Pradhan, A. K., & Rao, K. P. (2002). A novel Kalman filter for frequency estimation of distorted signals in power systems. IEEE Transactions on Instrumentation and Measurement, 51(3), 469-479.
[Badiu’17] M.-A. Badiu, T. L. Hansen, and B. H. Fleury, ”Variational Bayesian inference of line spectra," IEEE Trans. Signal Process., vol. 65, no. 9, pp. 2247-2261, 2017.
[Datta’10] B. N. Datta, Numerical linear algebra and applications. Siam, 2010.
[Djuric’95] P. M. Djuric and H.-T. Li, “Bayesian spectrum estimation of harmonic signals," IEEE Signal Process. Lett., vol. 2, no. 11, pp. 213-215, 1995.
[Hoang’18] M. Trinh-Hoang, M. Viberg, and M. Pesavento, “Partial relaxation approach: An eigenvalue-based DOA estimator framework,” IEEE Trans. Signal Process., vol. 66, no. 23, pp. 6190–6203, 2018.
[Hu’08] H. Fu and P. Y. Kam, ”MAP/ML estimation of the frequency and phase of a single sinusoid in noise," IEEE Trans. Signal Process., vol. 55, no. 3, pp. 834-845, 2007.
[Tenneti’19] S. V. Tenneti and P. P. Vaidyanathan, “imusic: A family of music-like algorithms for integer period estimation,” IEEE Trans. on Signal Process., vol. 67, no. 2, pp. 367–382, 2019.
Spectral Estimation
Instantaneous Frequency Estimation

## Slide 36: Bibliography
[Borgnat’10] P. Borgnat, P. Flandrin, P. Honeine, C. Richard, and J. Xiao, “Testing stationarity with surrogates: A time-frequency approach” IEEE Trans on Sig. Process, vol. 58, no. 7, pp. 3459–3470, 2010.
[Chau’05] T. Chau, D. Chau, M. Casas, G. Berall, and D. J. Kenny, “Investigating the stationarity of paediatric aspiration signals,” IEEE Trans. Neural Sys. and Rehabilitation Engg., vol. 13, no. 1, pp. 99–105, 2005.
[Chu’17] Y. Chu and C. M. Mak, “A new parametric adaptive nonstationarity detector and application," IEEE Trans. Signal Process. vol. 65, no. 19, pp. 5203-5214, 2017.
[Kay’08] S. Kay, “A new nonstationarity detector,” IEEE Trans on Sig. Process., vol. 56, no. 4, pp. 1440–1451, 2008.
[Rudoy’11] D. Rudoy, T. F. Quatieri, and P. J. Wolfe, “Time-varying Autoregressions in Speech: Detection Theory and Applications,"
IEEE Trans. Acoust., Speech, Signal Process., vol. 19, no. 4, pp. 977-989, 2011.
[Sanei’13] S. Sanei and J. A. Chambers, EEG signal processing. John Wiley & Sons, 2013.
[Dalvand’18] F. Dalvand, M. Kang, S. Dalvand, and M. Pecht, “Detection of generalized-roughness and single-point bearing faults using linear prediction-based current noise cancellation," IEEE Trans. Ind. Electron, vol. 65, no. 12, pp. 9728-9738, 2018.
[Delgado-Prieto’18] M. Delgado-Prieto, J. A. Carino-Corrales, J. J. Saucedo-Dorantes, R. de Jesus Romero-Troncoso, and R. A. Osornio-Rios, “Thermography-based methodology for multifault diagnosis on kinematic chain,” IEEE Trans. Ind. Inform., vol. 14, no. 12, pp. 5553-5562, 2018.
[Nandi’05] S. Nandi, H. A. Toliyat, and X. Li, “Condition Monitoring and Fault Diagnosis of Electrical Motors A Review," IEEE Trans. Energy Convers., vol. 20, no. 4, pp. 719-729, 2005
[Riera-Guasp’15] M. Riera-Guasp, J. A. Antonino-Daviu, and G.-A. Capolino, “Advances in Electrical Machine, Power Electronic, and Drive Condition Monitoring and Fault Detection: State of the Art," IEEE Trans. Ind. Electron., vol. 62, no. 3, pp. 1746-1759, 2015.
[Tu’19] X. Tu, Y. Hu, F. Li, S. Abbas, Z. Liu, and W. Bao, “Demodulated high-order synchro-squeezing transform with application to machine fault diagnosis,” IEEE Trans. Ind. Electron, vol. 66, no. 4, pp. 3071-3081, 2019.
[Zhao’19] R. Zhao, R. Yan, Z. Chen, K. Mao, P. Wang, and R. X. Gao, “Deep learning and its applications to machine health monitoring,“ Mech. Syst. Signal Process., vol. 115, pp. 213-237, 2019.
Fault Detection
Non-Stationarity Detection

## Slide 37
Thank you